## Slide 1: Intro to Digital Electronics

## Slide 2: Brief History of Digital Electronics
Digital electronics can be found in many applications in the form of microprocessors, microcontrollers, PCs, DSPs, and an uncountable number of other systems.
The historic development of design of digital circuits:
  resistor-transistor logic (RTL)
  diode-transistor logic (DTL)
  transistor-transistor logic (TTL)
  emitter-coupled logic (ECL)
  NMOS
  complementary MOS (CMOS)

## Slide 3: Digital Binary Logic
Digital electronics represent signals by discrete bands of analog levels, rather than by a continuous range.

## Slide 4: Digital Binary Logic
Digital electronics represent signals by discrete bands of analog levels, rather than by a continuous range.
All levels within a band represent the same signal state.
Small changes to the analog signal levels due to manufacturing tolerance, or noise do not leave the discrete envelope, and as a result are ignored by signal state sensing circuitry.

## Slide 5: Digital Binary Logic
Digital electronics represent signals by discrete bands of analog levels, rather than by a continuous range.
All levels within a band represent the same signal state.
Small changes to the analog signal levels due to manufacturing tolerance, or noise do not leave the discrete envelope, and as a result are ignored by signal state sensing circuitry.
Binary logic is the most common style of digital logic.
The signal is either a 0 (low, false) or a 1 (high, true) - Positive Logic Convention

## Slide 6: Digital Binary Logic
Digital electronics represent signals by discrete bands of analog levels, rather than by a continuous range.
All levels within a band represent the same signal state.
Small changes to the analog signal levels due to manufacturing tolerance, or noise do not leave the discrete envelope, and as a result are ignored by signal state sensing circuitry.
Binary logic is the most common style of digital logic.
The signal is either a 0 (low, false) or a 1 (high, true) - Positive Logic Convention
Mathematical representation of logical operations is Boolean algebra: set of operations (NOT, AND, OR, NAND, NOR, etc.) with binary or logical elements.
To perform general logical operations, a logic family must contain NOT and at least one another function of two inputs OR or AND.

## Slide 7: Review of Boolean Algebra
A | Z
0 | 1
1 | 0
A | B | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
NOT
Truth Table
OR
Truth Table
AND
Truth Table
A | B | Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR
Truth Table
NAND
Truth Table

## Slide 8: Review of Boolean Algebra
A | Z
0 | 1
1 | 0
A | B | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
NOT
Truth Table
OR
Truth Table
AND
Truth Table
A | B | Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR
Truth Table
NAND
Truth Table

## Slide 9: Review of Boolean Algebra
A | Z
0 | 1
1 | 0
A | B | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
NOT
Truth Table
OR
Truth Table
AND
Truth Table
A | B | Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR
Truth Table
NAND
Truth Table

## Slide 10: Review of Boolean Algebra
A | Z
0 | 1
1 | 0
A | B | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
NOT
Truth Table
OR
Truth Table
AND
Truth Table
A | B | Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR
Truth Table
NAND
Truth Table

## Slide 11: Review of Boolean Algebra
A | Z
0 | 1
1 | 0
A | B | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
NOT
Truth Table
OR
Truth Table
AND
Truth Table
A | B | Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR
Truth Table
NAND
Truth Table

## Slide 12: Review of Boolean Algebra
A | Z
0 | 1
1 | 0
A | B | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
NOT
Truth Table
OR
Truth Table
AND
Truth Table
A | B | Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR
Truth Table
NAND
Truth Table
De Morgan's laws

## Slide 13: Logic Gate Symbols and Boolean Expressions
A logic gate is a physical model of a Boolean function: it performs a logical operation on one or more logic inputs and produces a single logic output.

## Slide 14: Logic Gates: AND
A = 0 , B = 0  both diodes are forward biased  both diodes conduct out is LOW  0.
The simples gates are AND and OR. They can be built from switches or using the simplest form of electronic logic - diode logic.

## Slide 15: Logic Gates: AND
A = 0 , B = 0  both diodes are forward biased  both diodes conduct out is LOW  0.
A = 0 , B = 1  DB is reverse biased  does not conduct,
DA is forward biased  conducts out is LOW  0.
The simples gates are AND and OR. They can be built from switches or using the simplest form of electronic logic - diode logic.

## Slide 16: Logic Gates: AND
A = 0 , B = 0  both diodes are forward biased  both diodes conduct out is LOW  0.
A = 0 , B = 1  DB is reverse biased  does not conduct,
DA is forward biased  conducts out is LOW  0.
A = 1 , B = 0  DA is reverse biased  does not conduct,
DB is forward biased  conducts out is LOW  0.
The simples gates are AND and OR. They can be built from switches or using the simplest form of electronic logic - diode logic.

## Slide 17: Logic Gates: AND
A = 0 , B = 0  both diodes are forward biased  both diodes conduct out is LOW  0.
A = 0 , B = 1  DB is reverse biased  does not conduct,
DA is forward biased  conducts out is LOW  0.
A = 1 , B = 0  DA is reverse biased  does not conduct,
DB is forward biased  conducts out is LOW  0.
A = 1 , B = 1  both diodes are reverse biased 
both the diodes do not conduct  out is HIGH  1.
The simples gates are AND and OR. They can be built from switches or using the simplest form of electronic logic - diode logic.

## Slide 18: Logic Gates: OR
A = 0 , B = 0  both diodes are reverse biased  does not conduct out is LOW  0.
A = 0 , B = 1  DA is reverse biased  does not conduct,
DB is forward biased  conducts out is HIGH  1.
A = 1 , B = 0  DB is reverse biased  does not conduct,
DA is forward biased  conducts out is HIGH  1.
A = 1 , B = 1  both diodes are reverse biased 
both the diodes conduct  out is HIGH  1.

## Slide 19: Logic Gates: NAND & NOR
The simple diode logic allows AND and OR, but not inverters  an incomplete form of logic.
Also, without some kind of amplification it is not possible to have such basic logic operations cascaded as required for more complex logic functions.

## Slide 20: Logic Gates: NAND & NOR
The simple diode logic allows AND and OR, but not inverters  an incomplete form of logic.
Also, without some kind of amplification it is not possible to have such basic logic operations cascaded as required for more complex logic functions.
However, any gate can be built from NAND or NOR gates. This enables a circuit to be built from just one type of gate, either NAND or NOR.
To build NAND or NOR inverter is required  transistors needed.

## Slide 21: Logic Gates: NAND & NOR
The simple diode logic allows AND and OR, but not inverters  an incomplete form of logic.
Also, without some kind of amplification it is not possible to have such basic logic operations cascaded as required for more complex logic functions.
However, any gate can be built from NAND or NOR gates. This enables a circuit to be built from just one type of gate, either NAND or NOR.
To build NAND or NOR inverter is required  transistors needed.
Conclusion.
To build a functionally complete logic systems transistors are used.
The most basic digital building block is the inverter.

## Slide 22: Diode-Transistor Logic (DTL) Gate
The inversion and level-restoration problem associated with diode logic can be solved by adding a diode and transistor to form the diode-transistor logic (DTL) gate
It will be analyzed in detail sin Chapter 9; here is a brief overview.

## Slide 23: Diode-Transistor Logic (DTL) Gate
On the left, diodes D1 and D2 are both off, whereas D3 and Q1 are on. Node 1 is at 1.3 V:
V1 = VD3 + VBE = 0.6 V + 0.7 V = 1.3 V
The current I through resistor RB and diode D3 becomes the base current IB of transistor Q1. The
value of IB is designed to cause Q1 to saturate so that vO = VCESAT (for example, 0.05 to 0.1 V).
The inversion and level-restoration problem associated with diode logic can be solved by adding a diode and transistor to form the diode-transistor logic (DTL) gate
It will be analyzed in detail sin Chapter 9; here is a brief overview.

## Slide 24: Diode-Transistor Logic (DTL) Gate
On the right, input B is now at 0 V, corresponding to a logical 0. Diode D2 is conducting,
holding node 1 at 0.6 V. Now diode D3 and transistor Q1 must both be off, because the voltage at
node 1 is now less than the two diode voltage drops required to turn on both D3 and Q1. The base
current of Q1 is now zero; Q1 will be off with IC = 0, and the output voltage will be at +3.3 V,
corresponding to a logical 1. A similar situation holds for the circuit if both inputs are low.
The inversion and level-restoration problem associated with diode logic can be solved by adding a diode and transistor to form the diode-transistor logic (DTL) gate
It will be analyzed in detail sin Chapter 9; here is a brief overview.

## Slide 25: Diode-Transistor Logic (DTL) Gate
On the left, diodes D1 and D2 are both off, whereas D3 and Q1 are on. Node 1 is at 1.3 V:
V1 = VD3 + VBE = 0.6 V + 0.7 V = 1.3 V
The current I through resistor RB and diode D3 becomes the base current IB of transistor Q1. The
value of IB is designed to cause Q1 to saturate so that vO = VCESAT (for example, 0.05 to 0.1 V).
On the right, input B is now at 0 V, corresponding to a logical 0. Diode D2 is conducting,
holding node 1 at 0.6 V. Now diode D3 and transistor Q1 must both be off, because the voltage at
node 1 is now less than the two diode voltage drops required to turn on both D3 and Q1. The base
current of Q1 is now zero; Q1 will be off with IC = 0, and the output voltage will be at +3.3 V,
corresponding to a logical 1. A similar situation holds for the circuit if both inputs are low.
The inversion and level-restoration problem associated with diode logic can be solved by adding a diode and transistor to form the diode-transistor logic (DTL) gate
It will be analyzed in detail sin Chapter 9; here is a brief overview.

## Slide 26: The Ideal Inverter
The ideal inverter has the following voltage transfer characteristic (VTC) and is described by the following symbol
?

## Slide 27: The Ideal Inverter
The ideal inverter has the following voltage transfer characteristic (VTC) and is described by the following symbol
V+ and V- are the supply rails
VH and VL describe the high and low logic levels at the output

## Slide 28: Inverter - circuit
An inverter operating with power supplies at V+ and 0 V can be implemented using a switch with a resistive load.
?
MOSFET

## Slide 29: Inverter - circuit
An inverter operating with power supplies at V+ and 0 V can be implemented using a switch with a resistive load.
?
Q-point

## Slide 30: Inverter - circuit
An inverter operating with power supplies at V+ and 0 V can be implemented using a switch with a resistive load.
Q-point

## Slide 31: Inverter - circuit
An inverter operating with power supplies at V+ and 0 V can be implemented using a switch with a resistive load.

## Slide 32: VTC of Non-Ideal Inverter Voltage Level Definitions
For the (VTC) of the non-ideal inverter no Vref is defined. There is now an undefined logic state. The points (VIH ,VOL ) and (VIL ,VOH ) are defined as the points on the VTC curve where slope is -1.

## Slide 33: Logic Voltage Level Definitions
VL – The nominal voltage corresponding to a low-logic
state at the output of a logic gate for vi = VH

## Slide 34: Logic Voltage Level Definitions
VL – The nominal voltage corresponding to a low-logic
state at the output of a logic gate for vi = VH
VH – The nominal voltage corresponding to a high-logic
state at the output of a logic gate for vi = VL

## Slide 35: Logic Voltage Level Definitions
VL – The nominal voltage corresponding to a low-logic
state at the output of a logic gate for vi = VH
VH – The nominal voltage corresponding to a high-logic
state at the output of a logic gate for vi = VL
VIL – The maximum input voltage that will be recognized
as a low input logic level

## Slide 36: Logic Voltage Level Definitions
VL – The nominal voltage corresponding to a low-logic
state at the output of a logic gate for vi = VH
VH – The nominal voltage corresponding to a high-logic
state at the output of a logic gate for vi = VL
VIL – The maximum input voltage that will be recognized
as a low input logic level
VIH – The minimum input voltage that will be recognized
as a high input logic level

## Slide 37: Logic Voltage Level Definitions
VL – The nominal voltage corresponding to a low-logic
state at the output of a logic gate for vi = VH
VH – The nominal voltage corresponding to a high-logic
state at the output of a logic gate for vi = VL
VIL – The maximum input voltage that will be recognized
as a low input logic level
VIH – The minimum input voltage that will be recognized
as a high input logic level
VOH – The output voltage corresponding to an input
voltage of VIL

## Slide 38: Logic Voltage Level Definitions
VL – The nominal voltage corresponding to a low-logic
state at the output of a logic gate for vi = VH
VH – The nominal voltage corresponding to a high-logic
state at the output of a logic gate for vi = VL
VIL – The maximum input voltage that will be recognized
as a low input logic level
VIH – The minimum input voltage that will be recognized
as a high input logic level
VOH – The output voltage corresponding to an input
voltage of VIL
VOL – The output voltage corresponding to an input
voltage of VIH

## Slide 39: Logic Voltage Level Definitions
VL – The nominal voltage corresponding to a low-logic
state at the output of a logic gate for vi = VH
VH – The nominal voltage corresponding to a high-logic
state at the output of a logic gate for vi = VL
VIL – The maximum input voltage that will be recognized
as a low input logic level
VIH – The minimum input voltage that will be recognized
as a high input logic level
VOH – The output voltage corresponding to an input
voltage of VIL
VOL – The output voltage corresponding to an input
voltage of VIH
Typically, V-=0.
V+=5 for bipolar logic,
V+=1.8, 2.5, 3.3 for MOS logic
V+=1.0-1.5 for ultra low voltage logic

## Slide 40: Noise Margins
Noise margins represent “safety margins” that prevent the circuit from producing erroneous outputs in the presence of noisy inputs
Noise margins are defined for low and high input levels using the following equations:
NML = VIL – VOL
NMH = VOH – VIH

## Slide 41: Logic Gate Design Goals
An ideal logic gate is highly nonlinear and attempts to quantize the input signal to two discrete states. In an actual gate, the designer should attempt to minimize the undefined input region while maximizing noise margins

## Slide 42: Logic Gate Design Goals
An ideal logic gate is highly nonlinear and attempts to quantize the input signal to two discrete states. In an actual gate, the designer should attempt to minimize the undefined input region while maximizing noise margins
The logic gate is unidirectional. Changes at the output should have no effect on the input.

## Slide 43: Logic Gate Design Goals
An ideal logic gate is highly nonlinear and attempts to quantize the input signal to two discrete states. In an actual gate, the designer should attempt to minimize the undefined input region while maximizing noise margins
The logic gate is unidirectional. Changes at the output should have no effect on the input.
Voltage levels at the output of one gate should be compatible with the input levels of a following gate

## Slide 44: Logic Gate Design Goals
An ideal logic gate is highly nonlinear and attempts to quantize the input signal to two discrete states. In an actual gate, the designer should attempt to minimize the undefined input region while maximizing noise margins
The logic gate is unidirectional. Changes at the output should have no effect on the input.
Voltage levels at the output of one gate should be compatible with the input levels of a following gate
The output of one gate should be capable of driving the input of more than one gate: the gate should have sufficient fan-out and fan-in capabilities

## Slide 45: Logic Gate Design Goals
An ideal logic gate is highly nonlinear and attempts to quantize the input signal to two discrete states. In an actual gate, the designer should attempt to minimize the undefined input region while maximizing noise margins
The logic gate is unidirectional. Changes at the output should have no effect on the input.
Voltage levels at the output of one gate should be compatible with the input levels of a following gate
The output of one gate should be capable of driving the input of more than one gate: the gate should have sufficient fan-out and fan-in capabilities
The gate should consume minimal power (and area for ICs) and still operate under the design specifications

## Slide 46: Dynamic Response of Logic Gates
An important characteristic of the logical gates is the response in the time domain
To describe the typical pulse signal at the input, we introduce:
The rise and fall times: tf and tr, are measured at the 10% and 90% points on the transitions between the two states as shown by the following expressions:
V10% = VL + 0.1V
V90% = VL + 0.9V = VH – 0.1V
where V is the logic swing given by V = VH - VL

## Slide 47: Dynamic Response of Logic Gates
For the input on the top, will the output will be like the signal on the bottom plot?

## Slide 48: Dynamic Response of Logic Gates
For the input on the top, will the output will be like the signal on the bottom plot?
No, It will be delayed.

## Slide 49: Dynamic Response of Logic Gates
For the input on the top, will the output will be like the signal on the bottom plot?
No, It will be delayed.
Propagation delay describes the amount of time between the input reaching the 50% point and the output reaching the 50% point. The 50% point is described by the following:
The high-to-low propagation delay, PHL, and the low-to-high propagation delay, PLH, are usually not equal, but can be combined as an average value:

## Slide 50: NMOS Logic Design
MOS transistors (both PMOS and NMOS) can be combined with resistive loads to create single channel logic gates.

## Slide 51: NMOS Logic Design
MOS transistors (both PMOS and NMOS) can be combined with resistive loads to create single channel logic gates.
In most logic design situations, the power supply voltage is predetermined by either technology reliability constraints or system-level criteria
The circuit designer is limited to altering circuit topology and the width-to-length (W/L) ratio since the other factors are dependent upon processing parameters

## Slide 52: NMOS Logic Design
MOS transistors (both PMOS and NMOS) can be combined with resistive loads to create single channel logic gates.
In most logic design situations, the power supply voltage is predetermined by either technology reliability constraints or system-level criteria
The circuit designer is limited to altering circuit topology and the width-to-length (W/L) ratio since the other factors are dependent upon processing parameters
We begin our study of MOS logic circuit design by considering the detailed design of the NMOS inverter with the resistor load.

## Slide 53: NMOS Logic Design
MOS transistors (both PMOS and NMOS) can be combined with resistive loads to create single channel logic gates.
In most logic design situations, the power supply voltage is predetermined by either technology reliability constraints or system-level criteria
The circuit designer is limited to altering circuit topology and the width-to-length (W/L) ratio since the other factors are dependent upon processing parameters
We begin our study of MOS logic circuit design by considering the detailed design of the NMOS inverter with the resistor load.
In integrated logic circuits, the load resistor occupies too much silicon area, and is replaced by a second NMOS transistor. This “load device” can be connected in three different configurations called the saturated load, linear load, and depletion-mode load circuits.

## Slide 54: NMOS Inverter with a Resistive Load
The basic inverter circuit consists of an NMOS switching device MS and a resistor load element.
MS is the switching transistor used to “pull” the output high - toward to the power supply VDD
The resistor R is used to “pull” the output low, to force vO to VL
The size of R and the W/L ratio of MS are the design factors that need to be chosen.

## Slide 55: NMOS Inverter with a Resistive Load
When the input voltage is at a low state, vI = VL , MS should be cut off, with iD = 0, so that
vO = VDD = VH
Thus, in this particular logic circuit, the value of VH is set by the power supply voltage VDD = 2.5V.
To ensure that switching transistor MS is cut off when the input is in the low logic state, VL is designed to be 25 to 50 percent of the threshold voltage VTN of switch MS. This choice also provides a reasonable value for noise margin NML .
The equation for the output voltage (load line): vO = vDS = VDD − iD R

## Slide 56: NMOS Inverter with a Resistive Load
When the input voltage is at a low state, vI = VL , MS should be cut off, with iD = 0, so that
vO = VDD = VH
Thus, in this particular logic circuit, the value of VH is set by the power supply voltage VDD = 2.5V.
To ensure that switching transistor MS is cut off when the input is in the low logic state, VL is designed to be 25 to 50 percent of the threshold voltage VTN of switch MS. This choice also provides a reasonable value for noise margin NML .
When the input voltage is at a high state, vI = VH , switch MS is set in the triode region by the design of W/L parameter and load line to ensure that vO = VL.
The equation for the output voltage (load line): vO = vDS = VDD − iD R

## Slide 57: NMOS with Resistive Load Design Example (1)
Design a NMOS resistive load inverter for
  VDD = 3.3 V
  P = 0.1 mW when VL = 0.2 V
  Kn = 60 A/V2
  VTN = 0.75 V
Find the value of the load resistor R and the W/L ratio of the switching transistor MS

## Slide 58: NMOS with Resistive Load Design Example (2)
First the value of the current through the resistor (for vO = VL) must be determined by using the following:
The value of the resistor can now be found by the following, which assumes that the transistor is on and the output is low:

## Slide 59: NMOS with Resistive Load Design Example (3)
For vI = VH = 3.3 V, and vO = VL = 0.2V, the transistor’s drain-source voltage VDS =VL will be less than VGS -VTN=VH -VTN
Therefore it will be operating in the triode region. Using the triode region equation for the MOSFET, the W/L ratio can be found:

## Slide 60: On-Resistance of the Switching Device
The NMOS resistive load inverter can be thought of as a resistive voltage divider when the output is low:
where the On-Resistance Ron of the NMOS can be calculated with the following expression:
Note : 1. Ron should be kept small compared to R to ensure that VL remains low. 2. Its value is nonlinear, since it has a dependence on vDS.

## Slide 61: Noise Margin Analysis
The following equations (base on the calculation of the derivatives of vO =VDD –iDR with respect to vI ) can be used to determine the various parameters needed to determine the noise margin of NMOS resistive load inverters

## Slide 62: Load Resistor Issue
For completely integrated circuits, R must be implemented on chip using the shown structure.

## Slide 63: Load Resistor Issue
For completely integrated circuits, R must be implemented on chip using the shown structure.
If the resistor width W were made a line width of 1mm (minimum feature size F), then the length L would be 2880 mm, and the area would be 2880 mm2.

## Slide 64: Load Resistor Issue
For completely integrated circuits, R must be implemented on chip using the shown structure.
If the resistor width W were made a line width of 1mm (minimum feature size F), then the length L would be 2880 mm, and the area would be 2880 mm2.
For the transistor MS, W/L was found to be 2.22/1. If the device channel length is equal to the minimum feature size of 1 mm, then the gate area of the NMOS is only 2.22 mm2. Thus, the load resistor would consume more than 1000 times the area of the switching transistor MS.

## Slide 65: Load Resistor Issue
For completely integrated circuits, R must be implemented on chip using the shown structure.
If the resistor width W were made a line width of 1mm (minimum feature size F), then the length L would be 2880 mm, and the area would be 2880 mm2.
For the transistor MS, W/L was found to be 2.22/1. If the device channel length is equal to the minimum feature size of 1 mm, then the gate area of the NMOS is only 2.22 mm2. Thus, the load resistor would consume more than 1000 times the area of the switching transistor MS.
This is simply not an acceptable utilization of area in IC design.

## Slide 66: Load Resistor Issue
For completely integrated circuits, R must be implemented on chip using the shown structure.
If the resistor width W were made a line width of 1mm (minimum feature size F), then the length L would be 2880 mm, and the area would be 2880 mm2.
For the transistor MS, W/L was found to be 2.22/1. If the device channel length is equal to the minimum feature size of 1 mm, then the gate area of the NMOS is only 2.22 mm2. Thus, the load resistor would consume more than 1000 times the area of the switching transistor MS.
This is simply not an acceptable utilization of area in IC design.
The solution to this problem is to replace the load resistor with a transistor.

## Slide 67: Using Transistors in Place of a Resistor
NMOS load transistor with
a) gate connected to the source
b) gate connected to ground
c) gate connected to VDD
d) gate biased to linear region
e) a depletion-mode NMOSFET
f) gate grounded PMOS load
We are replacing a 2-terminal device with a 3(4)-terminal device and need to figure our what to do with the gate (since drain and source are conducting).

## Slide 68: Using Transistors in Place of a Resistor
NMOS load with
a) gate connected to the source
b) gate connected to ground
c) gate connected to VDD
d) gate biased to linear region
e) a depletion-mode NMOSFET
f) gate grounded PMOS load
Note that a) and b) are not useful, since with 0 at the gate, the enhancement mode NMOS is not conducting.
We’ll consider other methods starting from (c)
We are replacing a 2-terminal device with a 3(4)-terminal device and need to figure our what to do with the gate (since drain and source are conducting).

## Slide 69: NMOS Saturated Load Inverter
Schematic for a NMOS
saturated load inverter
The substrate is common and grounded:
It’s the (c) on diagram, called saturated because ML is in saturation region:
vDS = vGS  vDS ≥ vGS − VTN for VTN ≥ 0

## Slide 70: NMOS Saturated Load Inverter
Schematic for a NMOS
saturated load inverter
The substrate is common and grounded:
 vSB=0 for MS .
It’s the (c) on diagram, called saturated because ML is in saturation region:
vDS = vGS  vDS ≥ vGS − VTN for VTN ≥ 0

## Slide 71: NMOS Saturated Load Inverter
Schematic for a NMOS
saturated load inverter
The substrate is common and grounded:
 vSB=0 for MS .
 vSB=vO for ML ,
It’s the (c) on diagram, called saturated because ML is in saturation region:
vDS = vGS  vDS ≥ vGS − VTN for VTN ≥ 0

## Slide 72: NMOS Saturated Load Inverter
Schematic for a NMOS
saturated load inverter
The substrate is common and grounded:
 vSB=0 for MS .
 vSB=vO for ML ,
thus VTN is generally different for both.
It’s the (c) on diagram, called saturated because ML is in saturation region:
vDS = vGS  vDS ≥ vGS − VTN for VTN ≥ 0

## Slide 73: NMOS Saturated Load Inverter-Design Strategy
Given VDD, VL, and the power level, find IDD from VDD and power.

## Slide 74: NMOS Saturated Load Inverter-Design Strategy
Given VDD, VL, and the power level, find IDD from VDD and power.
Assume MS off, and find high output voltage level VH

## Slide 75: NMOS Saturated Load Inverter-Design Strategy
Given VDD, VL, and the power level, find IDD from VDD and power.
Assume MS off, and find high output voltage level VH
Use the value of VH for the gate voltage of MS and calculate (W/L)S of the switching transistor based on the design values of IDD and VL

## Slide 76: NMOS Saturated Load Inverter-Design Strategy
Given VDD, VL, and the power level, find IDD from VDD and power.
Assume MS off, and find high output voltage level VH
Use the value of VH for the gate voltage of MS and calculate (W/L)S of the switching transistor based on the design values of IDD and VL
Use the value of VH for the gate voltage of MS and find (W/L)L of the load transistor based on IDD and VL

## Slide 77: NMOS Saturated Load Inverter-Design Strategy
Given VDD, VL, and the power level, find IDD from VDD and power.
Assume MS off, and find high output voltage level VH
Use the value of VH for the gate voltage of MS and calculate (W/L)S of the switching transistor based on the design values of IDD and VL
Use the value of VH for the gate voltage of MS and find (W/L)L of the load transistor based on IDD and VL
Check the operating region assumptions of MS and ML for vo = VL

## Slide 78: NMOS Saturated Load Inverter - Example
Design an saturated load inverter given the following specifications:

## Slide 79: NMOS Saturated Load Inverter - Example
First, set vi = VH ,vO = VL, MS - on, and find the value of the current through the resistor using the power :
Design an saturated load inverter given the following specifications:
LIN
SAT

## Slide 80: NMOS Saturated Load Inverter - Example
First, set vi = VH ,vO = VL, MS - on, and find the value of the current through the resistor using the power :
Now set vi = VL ,vO = VH, MS - off, ML - off and then, find VH (since now, VH is not equal VDD.) Why?
Design an saturated load inverter given the following specifications:

## Slide 81: NMOS Saturated Load Inverter - Example
First, set vi = VH ,vO = VL, MS - on, and find the value of the current through the resistor using the power :
Now set vi = VL ,vO = VH, MS - off, ML - off and then, find VH (since now, VH is not equal VDD.) Why?
When MS turns off from the on state, the current IDD will stop when the value of vGSL will reach VTNL, (vGS > VTN, for IDD to exist)
vGSL = VDD − vO = VTN  VH = VDD − VTN .
Thus, taking into account the body effect (g) and surface potential parameter (fF):
(The output cannot exceed the positive power supply voltage.)
Design an saturated load inverter given the following specifications:

## Slide 82: NMOS Saturated Load Inverter - Example
Now we can find W/L for both transistors MS and then ML.
Set vi = VH , vo = VL: MS is in the triode region (on) ML is in saturation (on).
Check the operating region. For the switch, VGS − VTN = 2.11 − 0.75 = 1.36 V, which is greater than VDS = 0.2 V, and the triode region assumption is correct. For the load device, VGS − VTN =3.1 − 0.81 = 2.29 V and is less than VDS = 3.1 V, which is consistent with the saturation region of operation.
LIN
SAT

## Slide 83: NMOS Saturated Load Inverter -Noise Margin
From the PSPICE simulation typical noise margins are:
NMH = VOH - VIH = 1.55 - 1.42 = 0.33 V
NML = VIL - VOL = 0.90 - 0.38 = 0.22 V
The detailed analysis of the noise margins for saturated load inverter is quite tedious. Instead, the PSPICE simulation can be used. Example:

## Slide 84: NMOS Inverter with a Linear Load
This inverter has a load transistor that is biased with VGG defined by the following:

## Slide 85: NMOS Inverter with a Linear Load
This inverter has a load transistor that is biased with VGG defined by the following:
This causes the load transistor to operate in the linear region:
vGSL − VTNL = VGG − vo − VTNL

## Slide 86: NMOS Inverter with a Linear Load
This inverter has a load transistor that is biased with VGG defined by the following:
This causes the load transistor to operate in the linear region:
vGSL − VTNL = VGG − vo − VTNL
≥ VDD + VTNL − vo − VTNL
≥ VDD − vo = vDSL
For this value of VGG, the output voltage in the high output state VH is equal to VDD:
MS -off, iD=0  vDSL=0 (linear region) 
vDSL= VDD − vo = VDD − VH =0  VH = VDD

## Slide 87: NMOS Inverter with a Linear Load
This inverter has a load transistor that is biased with VGG defined by the following:
This causes the load transistor to operate in the linear region:
vGSL − VTNL = VGG − vo − VTNL
≥ VDD + VTNL − vo − VTNL
≥ VDD − vo = vDSL
For this value of VGG, the output voltage in the high output state VH is equal to VDD:
MS -off, iD=0  vDSL=0 (linear region) 
vDSL= VDD − vo = VDD − VH =0  VH = VDD
The W/L ratios for MS and ML can be calculated as in previous section ( easier, since VH is equal to VDD)

## Slide 88: NMOS Inverter with a Depletion-mode Load
The saturated load and linear load circuits were used when all the devices had the same threshold voltages in early NMOS and PMOS technologies.
However, once ion-implantation technology was perfected, it became possible to selectively adjust the threshold of the load transistors to alter their characteristics to become those of NMOS depletion mode devices with VTN < 0.
D
E

## Slide 89: NMOS Inverter with a Depletion-mode Load
When MS is off (vI = VL ), the current iD =0, hence from the linear region (which is now possible even for vGSL =0 because of depletion mode) we have vDSL =0 (< vGSL - VTN >0) and output voltage rises to VH = VDD
The saturated load and linear load circuits were used when all the devices had the same threshold voltages in early NMOS and PMOS technologies.
However, once ion-implantation technology was perfected, it became possible to selectively adjust the threshold of the load transistors to alter their characteristics to become those of NMOS depletion mode devices with VTN < 0.
D
E
LIN
iD =0

## Slide 90: NMOS Inverter with a Depletion-mode Load
When MS is off (vI = VL ), the current iD =0, hence from the linear region (which is now possible even for vGSL =0 because of depletion mode) we have vDSL =0 (< vGSL - VTN >0) and output voltage rises to VH = VDD
For MS on and conducting (vI = VH ), vO = VL, ML is designed to be saturated (vDSL = 2.5 - vO > vGSL - VTN ) and MS , as usual, in the triode region.
The saturated load and linear load circuits were used when all the devices had the same threshold voltages in early NMOS and PMOS technologies.
However, once ion-implantation technology was perfected, it became possible to selectively adjust the threshold of the load transistors to alter their characteristics to become those of NMOS depletion mode devices with VTN < 0.
D
E
LIN
SAT

## Slide 91
Then we set input to VH a(both transistors on) and find W/L
To find (W/L)L given iDL (which we find from power requirements) we use the saturation mode for ML with vGS =0 :
To find (W/L)S where VH = VDD, use the same technique as used for the resistor load inverter:
NMOS Inverter with a Depletion-mode Load

## Slide 92: NMOS Inverter with a Depletion-mode Load - Noise Margins
From PSPICE simulation, typical noise margins are:
NMH = VOH - VIH = 2.35 - 1.45 = 0.90 V
NML = VIL - VOL = 0.93 - 0.50 = 0.43 V
The detailed analysis of the noise margins for saturated load inverter is quite tedious. Instead, the PSPICE simulation can be used. Example:

## Slide 93: Pseudo NMOS Inverter
It is possible to replace the load resistor with a PMOS transistor with its source connected to VDD, its drain connected to the output node and its gate grounded.
This circuit is called pseudo NMOS since circuit operates very similar to NMOS although has a PMOS in it.
LIN
SAT
For vo = VL (MS is on), ML is in the saturation region.

## Slide 94: Pseudo NMOS Inverter
For vo = VL (MS is on), ML is in the saturation region.
For vo = VH (MS is off) ML is in the triode region (i=0, 0=VDS < |VGS - VTN |=|2.5 - VTN |.
For this circuit, VH = VDD because ML is in the linear triode region and VDS =0 when MS is off.
It is possible to replace the load resistor with a PMOS transistor with its source connected to VDD, its drain connected to the output node and its gate grounded.
This circuit is called pseudo NMOS since circuit operates very similar to NMOS although has a PMOS in it.
LIN

## Slide 95: Pseudo NMOS Inverter
It is possible to replace the load resistor with a PMOS transistor with its source connected to VDD, its drain connected to the output node and its gate grounded.
This circuit is called pseudo NMOS since circuit operates very similar to NMOS although has a PMOS in it.
LIN
For vo = VL (MS is on), ML is in the saturation region.
For vo = VH (MS is off) ML is in the triode region (i=0, 0=VDS < |VGS - VTN |=|2.5 - VTN |.
For this circuit, VH = VDD because ML is in the linear triode region and VDS =0 when MS is off.

## Slide 96: Pseudo NMOS Inverter Design - Example
Design an pseudo NMOS inverter given the following specifications:

## Slide 97: Pseudo NMOS Inverter Design - Example
Design an pseudo NMOS inverter given the following specifications:
First calculate (W/L)P to limit inverter current to 80 uA.

## Slide 98: Pseudo NMOS Inverter Design - Example
Design an pseudo NMOS inverter given the following specifications:
First calculate (W/L)P to limit inverter current to 80 uA.
MS is on, ML is in saturation:
LIN
SAT

## Slide 99: Pseudo NMOS Inverter Design - Example
Now calculate (W/L)S for the same condition and current of 80 uA.
LIN
SAT

## Slide 100: Pseudo NMOS Inverter - Noise Margins
From SPICE simulation, typical noise margins are:
NMH = VOH - VIH = 2.33 - 1.58 = 0.75 V
NML = VIL - VOL = 0.95 - 0.49 = 0.46 V

## Slide 101: NMOS Inverter Summary
Resistive load inverter takes up too much area for and IC design.

## Slide 102: NMOS Inverter Summary
Resistive load inverter takes up too much area for and IC design.
The saturated load configuration is the simplest design, but VH never reaches VDD, and it has a slow switching speed.

## Slide 103: NMOS Inverter Summary
Resistive load inverter takes up too much area for and IC design.
The saturated load configuration is the simplest design, but VH never reaches VDD, and it has a slow switching speed.
The linear load inverter fixes the speed and logic level issues, but it requires an additional power supply for the load gate.

## Slide 104: NMOS Inverter Summary
Resistive load inverter takes up too much area for and IC design.
The saturated load configuration is the simplest design, but VH never reaches VDD, and it has a slow switching speed.
The linear load inverter fixes the speed and logic level issues, but it requires an additional power supply for the load gate.
The depletion-mode NMOS load requires the most processing steps, but needs small area to achieve the high speed, VH = VDD, and best combination of noise margins.

## Slide 105: NMOS Inverter Summary
Resistive load inverter takes up too much area for and IC design.
The saturated load configuration is the simplest design, but VH never reaches VDD, and it has a slow switching speed.
The linear load inverter fixes the speed and logic level issues, but it requires an additional power supply for the load gate.
The depletion-mode NMOS load requires the most processing steps, but needs small area to achieve the high speed, VH = VDD, and best combination of noise margins.
The Pseudo NMOS inverter offers the best speed with the lowest area.

## Slide 106: Typical Inverter Characteristics
 | Inverter w/ Resistor Load | Saturated Load Inverter | Linear Load Inverter | Inverter w/ Depletion-Mode Load | Pseudo-NMOS Inverter
VH (V) | 2.50 | 1.55 | 2.50 | 2.50 | 2.50
VL (V) | 0.20 | 0.20 | 0.20 | 0.20 | 0.20
NML (V) | 0.25 | 0.25 | 0.12 | 0.43 | 0.46
NMH (V) | 0.96 | 0.33 | 0.96 | 0.90 | 0.75
Relative Area | 2880 | 6.39 | 7.94 | 4.03 | 3.33

## Slide 107: Reference of NMOS Inverter Designs

## Slide 108: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.

## Slide 109: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.

## Slide 110: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.

## Slide 111: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.

## Slide 112: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.

## Slide 113: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.

## Slide 114: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.

## Slide 115: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.
The worst condition for the output low (to have it as low as possible) is when only one switch is closed (since Ron for both are in parallel).

## Slide 116: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.
The worst condition for the output low (to have it as low as possible) is when only one switch is closed (since Ron for both are in parallel).
Thus the M/L ratio should be chosen the same as for one switch.

## Slide 117: NOR Gates
To obtain the complete logical family we need inverter and AND or OR function, or just one NAND or NOR element.
This type of element can be easily created by replacing one switch with two switches in parallel for NOR or in series for NAND.
The worst condition for the output low (to have it as low as possible) is when only one switch is closed (since Ron for both are in parallel).
Thus the M/L ratio should be chosen the same as for one switch.
When both are closed, the VL at the output will be even lower then for one.

## Slide 118: NAND Gates

## Slide 119: NAND Gates

## Slide 120: NAND Gates

## Slide 121: NAND Gate Device Size Selection
Consider the equivalent of switching transistors in the ‘on” state as Ron.

## Slide 122: NAND Gate Device Size Selection
Consider the equivalent of switching transistors in the ‘on” state as Ron.
To keep the low voltage level comparable with simple inverter, the desired Ron of MA and MB must be 0.5Ron of MS switch.

## Slide 123: NAND Gate Device Size Selection
Consider the equivalent of switching transistors in the ‘on” state as Ron.
To keep the low voltage level comparable with simple inverter, the desired Ron of MA and MB must be 0.5Ron of MS switch.
This can be accomplished by approximately doubling (W/L)A and (W/L)B

## Slide 124: NAND Gate Device Size Selection
Consider the equivalent of switching transistors in the ‘on” state as Ron.
To keep the low voltage level comparable with simple inverter, the desired Ron of MA and MB must be 0.5Ron of MS switch.
This can be accomplished by approximately doubling (W/L)A and (W/L)B

## Slide 125: NAND Gate Device Size Selection (cont)
Two sources of error that arise are that 1) VSB’s and 2) VGS’s of the two transistors are not equal  the values of VTN should be adjusted (see problem 6.28)
The technique used to calculate the size of the load transistor for the NAND gate is exactly the same as for the depletion-load inverter.

## Slide 126
An advantage of NMOS technology is that it is simple to design complex logic functions based on the NOR and NAND gates.
Complex NMOS Logic Design

## Slide 127
An advantage of NMOS technology is that it is simple to design complex logic functions based on the NOR and NAND gates.
The typical problem that arises is the transistor sizing.
Complex NMOS Logic Design

## Slide 128
An advantage of NMOS technology is that it is simple to design complex logic functions based on the NOR and NAND gates.
The typical problem that arises is the transistor sizing.
There are two ways to find the W/L ratios of the switching transistors
  Use the worst-case path (most devices in series) and choose the W/L ratios to achieve the value of Ron equivalent to that of the inverter
Complex NMOS Logic Design

## Slide 129
An advantage of NMOS technology is that it is simple to design complex logic functions based on the NOR and NAND gates.
The typical problem that arises is the transistor sizing.
There are two ways to find the W/L ratios of the switching transistors
  Use the worst-case path (most devices in series) and choose the W/L ratios to achieve the value of Ron equivalent to that of the inverter
  Partitioning the circuit into a series sub-networks, and make the equivalent on-resistances equal
Complex NMOS Logic Design

## Slide 130: Complex NMOS Logic Design (1)
Example 1. Design a logic function:
Y = A + B(C + D)
Base inverter:

## Slide 131: Complex NMOS Logic Design (1)
Example 1. Design a logic function:
Y = A + B(C + D)
Base inverter:

## Slide 132: Complex NMOS Logic Design (1)
Example 1. Design logic function:
Y = A + B(C + D)
Base inverter:

## Slide 133: Complex NMOS Logic Design (1)
Example 1. Design logic function:
Y = A + B(C + D)
Base inverter:
Referring to the base inverter design, we have for the MS W/L=2.22/1 in order to maintain the low output of 0.20V

## Slide 134: Complex NMOS Logic Design (1)
Example 1. Design logic function:
Y = A + B(C + D)
Base inverter:
Referring to the base inverter design, we have for the MS W/L=2.22/1 in order to maintain the low output of 0.20V
We’ll have the same for MA (in parallel).

## Slide 135: Complex NMOS Logic Design (1)
Example 1. Design logic function:
Y = A + B(C + D)
Base inverter:
Referring to the base inverter design, we have for the MS W/L=2.22/1 in order to maintain the low output of 0.20V
We’ll have the same for MA (in parallel).
In another parallel branch we have a series connection, so MB and combination of MC and MD should have double width W/L=4.44/1

## Slide 136: Complex NMOS Logic Design (1)
Example 1. Design logic function:
Y = A + B(C + D)
Base inverter:
Referring to the base inverter design, we have for the MS W/L=2.22/1 in order to maintain the low output of 0.20V
We’ll have the same for MA (in parallel).
In another parallel branch we have a series connection, so MB and combination of MC and MD should have double width W/L=4.44/1
Finally, MC and MD are in parallel, so their W/L does not change.

## Slide 137: Complex NMOS Logic Design (2)
Example 2. Design logic function:
Y = A B + CDB = (A+CD)B
Base inverter :

## Slide 138: Complex NMOS Logic Design (2)
Example 2. Design logic function:
Y = A B + CDB = (A+CD)B
Base inverter :
The figure on the left shows the worst case method. The longest path is 3 transistors in series, so (W/L)=6.66 /1 is the size for each element in series.

## Slide 139: Complex NMOS Logic Design (2)
Example 2. Design logic function:
Y = A B + CDB = (A+CD)B
Base inverter :
The figure on the left shows the worst case method. The longest path is 3 transistors in series, so (W/L)=6.66 /1 is the size for each element in series. One MA is in parallel with two transistors, so its W/L is halved.

## Slide 140: Complex NMOS Logic Design (2)
Example 2. Design logic function:
Y = A B + CDB = (A+CD)B
Base inverter :
The figure on the left shows the worst case method. The longest path is 3 transistors in series, so (W/L)=6.66 /1 is the size for each element in series. One MA is in parallel with two transistors, so its W/L is halved.
The figure on the right shows the partitioning technique : the longest path is 2, so (W/L)= 4.44/1.

## Slide 141: Complex NMOS Logic Design (2)
Example 2. Design logic function:
Y = A B + CDB = (A+CD)B
Base inverter :
The figure on the left shows the worst case method. The longest path is 3 transistors in series, so (W/L)=6.66 /1 is the size for each element in series. One MA is in parallel with two transistors, so its W/L is halved.
The figure on the right shows the partitioning technique : the longest path is 2, so (W/L)= 4.44/1. However, now we put 2 series transistors MC and MD in parallel with MA , so their with is doubled.

## Slide 142: Static Power Dissipation
Static Power Dissipation is the average power dissipation of the logic gate for the high and low logic states. If the duty cycle is 50% it is:
IDDH = current in the circuit for vO = VH
IDDL = current in the circuit for vO = VL
Since IDDH = 0 for vO = VH :
If the duty cycle is different, 2 in the denominator should be changed appropriatly.

## Slide 143: Dynamic Power Dissipation
Dynamic Power Dissipation is the power dissipated during the process of charging and discharging the load capacitance connected to the logic gate
Discharging
Charging
?
?

## Slide 144: Dynamic Power Dissipation
Dynamic Power Dissipation is the power dissipated during the process of charging and discharging the load capacitance connected to the logic gate
Discharging
Charging
RL

## Slide 145: Dynamic Power Dissipation
Dynamic Power Dissipation is the power dissipated during the process of charging and discharging the load capacitance connected to the logic gate
Discharging
Charging
RS

## Slide 146: Dynamic Power Dissipation
Dynamic Power Dissipation is the power dissipated during the process of charging and discharging the load capacitance connected to the logic gate
Discharging
Charging
RL
RS

## Slide 147: Dynamic Power Dissipation
Based on the energy equation, the energy delivered to the capacitor can be found by:

## Slide 148: Dynamic Power Dissipation
Based on the energy equation, the energy delivered to the capacitor can be found by:
The energy stored by the capacitor is:

## Slide 149: Dynamic Power Dissipation
Based on the energy equation, the energy delivered to the capacitor can be found by:
The energy stored by the capacitor is:
The energy lost in the resistive elements is given by:

## Slide 150: Dynamic Power Dissipation
Based on the energy equation, the energy delivered to the capacitor can be found by:
The energy stored by the capacitor is:
The energy lost in the resistive elements is given by:
The total energy lost in the first charging and discharging of the capacitor through resistive elements is given by:

## Slide 151: Dynamic Power Dissipation
Based on the energy equation, the energy delivered to the capacitor can be found by:
The energy stored by the capacitor is:
The energy lost in the resistive elements is given by:
The total energy lost in the first charging and discharging of the capacitor through resistive elements is given by:
Thus, if the logic circuit is switching at a frequency f, the dynamic power dissipation is given by:

## Slide 152: Dynamic Power Dissipation
Based on the energy equation, the energy delivered to the capacitor can be found by:
The energy stored by the capacitor is:
The energy lost in the resistive elements is given by:
The total energy lost in the first charging and discharging of the capacitor through resistive elements is given by:
Thus, if the logic circuit is switching at a frequency f, the dynamic power dissipation is given by:
In the high speed logic circuits this component becomes dominant and constitutes the primary source of power dissipation in CMOS logic gates.

## Slide 153: Power Scaling in MOS Logic
With the transistor load, the current in both the load and switch transistors is determined by the similar expressions, e.g.:
By reducing the W/L of the load and switching transistors of an inverter, it is possible to reduce the power dissipation by the same factor without sacrificing VH and VL.
This same concept works for increasing the power which will increase the dynamic response.

## Slide 154: Power Scaling in MOS Logic
Original Saturated Load Inverter
Saturated Load inverter designed to operate at 1/3 the power
Original Depletion-Mode Inverter
Depletion-mode inverter designed to operate at twice the power

## Slide 155: Dynamic Behavior Capacitance in MOS Logic Circuits
The MOS device has capacitances CSB, CGS, CDB, and CGD that need to be considered for dynamic response analysis.

## Slide 156: Dynamic Behavior Capacitance in MOS Logic Circuits
The MOS device has capacitances CSB, CGS, CDB, and CGD that need to be considered for dynamic response analysis.
The capacitances seen at a node can be lumped together.

## Slide 157: Dynamic Behavior Capacitance in MOS Logic Circuits
The MOS device has capacitances CSB, CGS, CDB, and CGD that need to be considered for dynamic response analysis.
The capacitances seen at a node can be lumped together.
DC loading constraints are not usually important for MOS logic circuits since they normally drive capacitive loads (i.e. the gate of a MOS)

## Slide 158: Dynamic Behavior Capacitance in MOS Logic Circuits
The MOS device has capacitances CSB, CGS, CDB, and CGD that need to be considered for dynamic response analysis.
The capacitances seen at a node can be lumped together.
DC loading constraints are not usually important for MOS logic circuits since they normally drive capacitive loads (i.e. the gate of a MOS)
As the number of gates the output (fan-out) of a logic device has to drive increases, the load capacitance increases, and the time response degrades.

## Slide 159: Dynamic Behavior Capacitance in MOS Logic Circuits
The MOS device has capacitances CSB, CGS, CDB, and CGD that need to be considered for dynamic response analysis.
The capacitances seen at a node can be lumped together.
DC loading constraints are not usually important for MOS logic circuits since they normally drive capacitive loads (i.e. the gate of a MOS)
As the number of gates the output (fan-out) of a logic device has to drive increases, the load capacitance increases, and the time response degrades.
This notion implies that the fan-out that a logic circuit can drive will be limited by time delay tolerances of the circuit.

## Slide 160: Dynamic Response of the NMOS Inverter with a Resistive Load
Rise time is defined as the time for the output to change from 10% to 90% of the complete transition.
Closing switch: vI high  low
Charging capacitor

## Slide 161: Dynamic Response of the NMOS Inverter with a Resistive Load
Delay time τPLH is defined as the time required for the output to change 50: vO(τPLH) = VI + 0.5DV, which yields :
where R and C are the resistance and capacitance seen at the output.
For high-to-low transitions, the on resistance of MS, RonS, varies during the transition but an effective R, Reff, can be approximated as 1.7 RonS.
For low-to-high transitions, R is the load resistance (MS is off):

## Slide 162: Pseudo NMOS Inverter - Dynamic Response
The expressions for the propagation delays are the same as for resistive
Closing switch: vI high  low
Opening switch: vI low  high

## Slide 163: Pseudo NMOS Inverter - Dynamic Response Example
Find tf, tr, PHL, PLH for a pseudo NMOS inverter where:
  (W/L)S = 2.22/1 and (W/L)L = 1.11/1
  CLOAD = 1 pF
  VTN = 0.6 V and VTP = -0.6 V
  VDD = 2.5 V
  Kn = (2.06)(100 ´ 10-6 A/V2)
  KL = (1.11)(40 ´ 10-6 A/V2)

## Slide 164: Pseudo NMOS Inverter - Dynamic Response Example
Find tf, tr, PHL, PLH for a pseudo NMOS inverter where:
  (W/L)S = 2.22/1 and (W/L)L = 1.11/1
  CLOAD = 1 pF
  VTN = 0.6 V and VTP = -0.6 V
  VDD = 2.5 V
  Kn = (2.06)(100 ´ 10-6 A/V2)
  KL = (1.11)(40 ´ 10-6 A/V2)
First find the on-resistances of the two switch and load devices

## Slide 165: Pseudo NMOS Inverter - Dynamic Response Example
Find tf, tr, PHL, PLH for a pseudo NMOS inverter where:
  (W/L)S = 2.22/1 and (W/L)L = 1.11/1
  CLOAD = 1 pF
  VTN = 0.6 V and VTP = -0.6 V
  VDD = 2.5 V
  Kn = (2.06)(100 ´ 10-6 A/V2)
  KL = (1.11)(40 ´ 10-6 A/V2)
First find the on-resistances of the two switch and load devices
Now calculate delays from the Reff approximations:

## Slide 166: Comparison of Load Devices
The simulation results for all five inverters. The current has been normalized to 80 A for vo = VOL= 0.20 V
The saturated load devices have the poorest fall time since they have the lowest load current delivery
The saturated load devices also reach zero current before the output reaches 2.5 V
The linear load device is faster than the saturated load device, but about equal to the resistive load speed.
The fastest PLH is for the pseudo NMOS device as a result of the PMOS device

## Slide 167: PMOS Logic
PMOS logic circuits predated NMOS logic circuit, but were replaced since they operate at slower speeds
Resistive Load
Saturated Load
Linear Load
Depletion-Mode Load
Pseudo PMOS

## Slide 168: PMOS NAND and NOR Gates
NOR Gate
NAND Gate