## Slide 1: Presentation on Sequential Logic
  Presented by
Israt Jahan Reshma
ID: 18ICTCSE041
Student of SHIICT,BSMRSTU
Course Title: Digital Logic Design

## Slide 2: 1. Design of a sequential circuit with two JK flip-flops and one input, x. When x = 0, the state of the circuit remains the same. When x = 1, the circuit goes through the state transitions from00 to 01 to 11 to 10 back to 00, and repeats.
Here, No State are equivalent, so, State reduction is not needed.
Present State |  | Next State |  |  | 
 |  | X=0 |  | X=1 | 
A | B | A | B | A | B
O | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0
Soln:

## Slide 3: K map for JA: k map for KA:
Present State |  | Input | Next State |  | Flip Flop Input |  |  | 
A | B | x | A | B | JA | KA | KB | KB
0 | 0 | 0 | 0 | 0 | 0 | X | 0 | X
0 | 0 | 1 | 0 | 1 | 0 | X | 1 | X
0 | 1 | 0 | 0 | 1 | 0 | X | X | 0
0 | 1 | 1 | 1 | 1 | 1 | X | X | 0
1 | 0 | 0 | 1 | 0 | X | 0 | 0 | X
1 | 0 | 1 | 0 | 0 | X | 1 | 0 | X
1 | 1 | 0 | 1 | 1 | X | 0 | X | 0
1 | 1 | 1 | 1 | 0 | X | 0 | X | 1
JA = Bx
KA = B’x

## Slide 4
The Logic Diagram:
K map for KB
KB= Ax
JB = A’x
K map for JB

## Slide 5: 2. Design of a counter with the following repeated binary sequence: 0, 1, 2, 4, 6 using JK flip-flops.
Present state |  |  | Next state |  |  | FF inputs |  |  |  |  | 
A | B | C | A | B | C | JA | KA | JB | KB | JC | KC
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X | X | 1
0 | 1 | 0 | 1 | 0 | 0 | 1 | X | X | 1 | 0 | X
0 | 1 | 1 | X | X | X | X | X | X | X | X | X
1 | 0 | 0 | 1 | 1 | 0 | X | 0 | 1 | X | 0 | X
1 | 0 | 1 | X | X | X | X | X | X | X | X | X
1 | 1 | 0 | 0 | 0 | 0 | X | 1 | X | 1 | 0 | X
1 | 1 | 1 | X | X | X | X | X | X | X | X | X
Soln:

## Slide 6
K map for JA
K map for KA
K map for JB
K map for KB
K map for JC
K map for KC
JA=B
KA=B
JB=AB’+B’C=B’(A+C)
KB=B
JC=A’B’
KC=1

## Slide 7
Present state |  |  | Next state |  |  | FF inputs |  |  |  |  | 
A | B | C | A(t+1) | B(t+) | C(t+1) | JA | KA | JB | KB | JC | KC
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
For unused steps:
Now we find A(t+1), B(t+1),C(t+1) from the equation of JA,KA,JB,KB,JC,KC.
we know,
A(t+1)=AK’+A’J
B(t+1)=BK’+B’J
C(t+1)=CK’+C’J

## Slide 8
The Logic Diagram:

## Slide 9: 3. Design of a counter with the following repeated binary sequence: 0, 1, 3, 7, 6, 4 using T flip-flops.
Present State |  |  | Next State |  |  | Flip Flop Inputs |  | 
A | B | C | A(t+1) | B(t+1) | C(t+1) | TA | TB | TC
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | X | X | X | X | X | X
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | X | X | X | X | X | X
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1
Soln:

## Slide 10: For unused steps: Now we find A(t+1), B(t+1),C(t+1) from the equation of TA,TB,TC. we know, A(t+1)=TA’+T’A B(t+1)=TB’+T’B C(t+1)=TC’+T’C
K map for TB
K map for TA
K map for TC
TA = A’B+AB’
= A
TB = B’C+BC’
= B
TC = A’C’+AC
= (A
Present State |  |  | Next State |  |  | Flip Flop Inputs |  | 
A | B | C | A(t+1) | B(t+1) | C(t+1) | TA | YB | TC
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1

## Slide 11
State Table After correction:
State Diagram:
Lock out problem
To solve this problem ,let us assume the following diagram
Present State |  |  | Next State |  |  | Flip Flop Inputs |  | 
A | B | C | A(t+1) | B(t+1) | C(t+1) | TA | YB | TC
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 12
K map for TA
K map for TB
K map for TC
TA = A’B+AB’
= A
TB = B’C+BC’
= B
TC = A’B’C’+AC
The Logic Diagram:

## Slide 13: 4. To reduce the number of the states in the following state table and tabulate the reduced state table.
present state | next state |  | output | 
 | x=0 | x=1 | x=0 | x=1
a | f | b | 0 | 0
b | d | c | 0 | 0
c | f | e | 0 | 0
d | g | a | 1 | 0
e | d | c | 0 | 0
f | f | b | 1 | 1
g | g | h | 0 | 1
h | g | a | 1 | 0

## Slide 14
present state | next state |  | output | 
 | x=0 | x=1 | x=0 | x=1
a | f | b | 0 | 0
b | d | c=a | 0 | 0
c | f | e=b | 0 | 0
d | g | a | 1 | 0
e | d | c | 0 | 0
f | f | b | 1 | 1
g | g | h=d | 0 | 1
h | g | a | 1 | 0
l
×
(h=d)
×
×
(e=b)
(c=a)

## Slide 15
Reduced State Table:
present state | next state |  | output | 
 | x=0 | x=1 | x=0 | x=1
a | f | b | 0 | 0
b | d | a | 0 | 0
d | g | a | 1 | 0
f | f | b | 1 | 1
g | g | d | 0 | 1

## Slide 16: 5. Design of a sequential circuit that has three D flip-flops A, B, C; one input, x and one output, y using the following state diagram
The State Table:
Present State |  |  | Input | Next State |  |  | output
A | B | C | x | A(t+1) | B(t+1) | C(t+1) | y
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
Soln:

## Slide 17: don’t care, d(A,B,C,x) = Ʃ(10,11,12,13,14,15)
K map for B(t+1)
K map for C(t+1)
K map for y
K map for A(t+1)
C(t+1)= A’B’x’+Cx’+Ax
B(t+1)= C’x’+A+BCx
y= A’x
A(t+1)= A’B’x
The Logic Diagram:

## Slide 18
Thank You