## Slide 1: Digital Logic Design
Chapter 1
Binary Systems

## Slide 2: Complements
Two types of complements:
  The r’s complement
  The (r-1)’s complement
The r’s complement:
Given a positive number N in base r with an integer part of n digits, the r’s complement of N is defined as rn – N for N ≠ 0.
10’s complement of (52520)10 is 10n – 52520 = 47480.
10’s complement of (0.3267)10 is 1 – 0.3267 = 0.6733.
No integer part , so 10n = 100 = 1

## Slide 3: Complements
The (r-1)’s complement:
Given a positive number N in base r with an integer part of n digits and a fraction part of m digits, the (r-1)’s complement of N is defined as rn – r-m – N.
9’s complement of (52520)10 is 105 – 1 – 52520 = 99999 – 52520 = 47479.
No fraction part, so 10-m = 100 = 1
9’s complement of (0.3267)10 is 1 – 10-4 – 0.3267 = 0.9999 – 0.3267 = 0.6732.
No integer part, so 10n = 100 = 1

## Slide 4: Subtraction with r’s complements
The subtraction of two positive numbers M – N (both of base r), may be done as follows:
Add M to the r’s complement of N.
Inspect the result obtained in step 1 for an end carry:
  If end carry occurs, discard it.
  If end carry does not occur, take the r’s complement of the number obtained in step 1 and place a negative sign in front.

## Slide 5: Subtraction with r’s complements
Using 10’s complement, subtract 72532 – 3250.
M = 72532 72532
N = 3250
10’s complement of N = 96750 + 96750
1 69282
Answer: 69282
End carry

## Slide 6: Subtraction with r’s complements
Subtract (3250 – 72532)10.
M = 3250 03250
N = 72532
10’s complement of N = 27468 + 27468
30718
Answer: – 69282 = – (10’s complement of 30718)
No carry

## Slide 7: Subtraction with (r–1)’s complements
The subtraction of two positive numbers M – N (both of base r), may be done as follows:
Add M to (r – 1)’s complement of N.
Inspect the result obtained in step 1 for an end carry.
  If end carry occurs, add 1 to the least significant digit.
  If end carry does not occur, take the (r – 1)’s complement of the number obtained in step 1 and place a negative sign in front.

## Slide 8: Subtraction with (r–1)’s complements
Using 9’s complement, subtract 72532 – 3250.
M = 72532 72532
N = 3250
9’s complement of N = 96749 + 96749
1 69281
69282
Answer: 69282
End carry
+ 1

## Slide 9: Subtraction with (r–1)’s complements
Using 9’s complement, subtract 3250 – 72532.
M = 03250 03250
N = 72532
9’s complement of N = 27467 + 27467
30717
Answer: – 69282 = – (9’s complement of 30717).
No carry

## Slide 10: Binary Codes
Decimal Digit | (BCD) 8421 | Excess-3 | 84-2-1 | 2421
0 | 0000 | 0011 | 0000 | 0000
1 | 0001 | 0100 | 0111 | 0001
2 | 0010 | 0101 | 0110 | 0010
3 | 0011 | 0110 | 0101 | 0011
4 | 0100 | 0111 | 0100 | 0100
5 | 0101 | 1000 | 1011 | 1011
6 | 0110 | 1001 | 1010 | 1100
7 | 0111 | 1010 | 1001 | 1101
8 | 1000 | 1011 | 1000 | 1110
9 | 1001 | 1100 | 1111 | 1111