## Slide 1: Digital Logic Design
Chapter 2
Boolean Algebra and Logic gates

## Slide 2: Basic Theorems
Postulate 2 | (a) x + 0 = x | (b) x . 1 = x
Postulate 5 | (a) x + x’ = 1 | (b) x . x’ = 0
Theorem 1 | (a) x + x = x | (b) x . x = x
Theorem 2 | (a) x + 1 = 1 | (b) x . 0 = 0
Theorem 3, involution | (x’)’ = x | 
Postulate 3, commutative | (a) x + y = y +x | (b) xy = yx
Theorem 4, associative | (a) x+ (y+z) = (x+y) + z | (b) x(yz) = (xy)z
Postulate 4, distributive | (a) x(y+z) = xy + xz | (b) x + yz = (x+y)(x+z)
Theorem 5, DeMorgan | (a) (x + y)’ = x’y’ | (b) (xy)’ = x’ + y’
Theorem 6, absorption | (a) x + xy = x | (b) x(x + y) = x

## Slide 3: Boolean Function
A binary variable can take the value 0 or 1.
A Boolean function is an expression formed with binary variables, the two binary operators OR and AND, the unary operator NOT, parentheses and equal sign.
For example: F1 = xyz’ , F2 = x + y’z
A Boolean function may also be represented in a truth table. To represent a function in a truth table, we need a list of 2n combinations of 1’s and 0’s of the n binary variables and a column showing the combinations for which the function is equal to 1 or 0.

## Slide 4: Boolean Function
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0
Truth tables for F1 = xyz’, F2 = x + y’z, F3 = x’y’z + x’yz + xy’ and F4 = xy’ + x’z

## Slide 5: Boolean Function
Simplify the following Boolean functions to a minimum number of literals.
x’y’z + x’yz + xy’
= x’z(y’ + y) + xy’
= x’z + xy’
xy + x’z + yz
= xy + x’z + yz(x + x’)
= xy + x’z + xyz + x’yz
= xy(1 + z) + x’z(1 + y)
= xy + x’z

## Slide 6: Complement of a Function
Find the complement of the functions F1 = x’yz’ + x’y’z
F1’ = (x’yz’ + x’y’z)’
= (x’yz’)’(x’y’z)’
= (x + y’ + z)(x + y + z’)
Find the complement of the functions F2 = x(y’z’ + yz)
F2’ = (x(y’z’ + yz))’
= x’ + (y’z’ + yz)’
= x’ + (y’z’)’(yz)’
= x’ + (y + z)(y’ + z’)

## Slide 7: Other Logic Operations

## Slide 8: Digital Logic Gates

## Slide 9: Digital Logic Gates

## Slide 10: Canonical & Standard Forms
Minterms & Maxterms:
Let us consider two binary variables x and y combined with an AND operation.
Since each variable may appear either in its normal form or in its complement form, there are four combinations: x’y’, x’y, xy’ and xy.
Each of these four AND terms represents a minterm.
Similarly, n variables forming an OR term, with each variable being primed or umprimed, provide 2n possible combinations, called maxterms.

## Slide 11: Canonical & Standard Forms
Boolean functions expressed as a sum of minterms or product of maxterms are said to be in Canonical form.
For example:
f1 = x’y’z + xy’z’ + xyz
= m1 + m4 + m7
f2 = (x+y+z)(x+y+z’)(x+y’+z)(z’+y+z)
= M0M1M2M4

## Slide 12: Canonical & Standard Forms
The terms that form a Boolean function may contain one, two or any number of literals. These are said to be in standard forms.
Two types of standard forms:
  Sum of products
  Product of sums
For example:
F1 = y’ + xy + x’yz’
F2 = x(y’+z)(x’+y+z’)

## Slide 13: Conversion Between Canonical Forms
Let a function be F(A, B, C) = Ʃ(1, 4, 5, 6, 7)
The function has a complement that can be expressed as:
F’(A, B, C) = Ʃ(0, 2, 3) = m0 + m2 + m3
Now if we take the complement of F’ by DeMorgan’s theorem, we obtain F in a different form:
F = (m0 + m2 + m3)’ = m0’.m2’.m3’ = M0M2M3
= Π(0, 2, 3)
Similarly, for the function F(x, y, z) = Π(0, 2, 4, 5), the conversion to sum of mintems is:
F(x, y, z) = Ʃ(1, 3, 6, 7)