## Slide 1: Digital Logic Design
Chapter 3
Simplification of Boolean Functions

## Slide 2: The Map Method
The map method provides a simple straightforward procedure for minimizing Boolean functions.
This method may be regarded either as a pictorial form of a truth table or as an extension of the Venn diagram.
The map method, first proposed by Veitch and modified by Karnaugh, is also known as the “Veitch diagram” or the “Karnaugh map”.

## Slide 3: Two- and Three-Variable Maps
There are four minterms for two variables; hence the map consists of four squares, one for each minterm.
A 1 is placed in the square of the minterm which is contained in the function. Otherwise 0 is placed.
y x | 0 | 1
0 | m0 | m1
1 | m2 | m3
y x | 0 | 1
0 | x’y’ | x’y
1 | xy’ | xy

## Slide 4: Two- and Three-Variable Maps
For example: f = x + y
= x’y + xy’ + xy
= m1 + m2 + m3
y x | 0 | 1
0 | 0 | 1
1 | 1 | 1

## Slide 5: Two- and Three-Variable Maps
There are eight minterms for three binary variables. Therefore, a map consists of eight squares.
The minterms are not arranged in a binary sequence, but in a sequence similar to the Gray code.
yz x | 00 | 01 | 11 | 10
0 | m0 | m1 | m3 | m2
1 | m4 | m5 | m7 | m6

## Slide 6: Two- and Three-Variable Maps
Simplify the Boolean function:
F(x, y, z) = x’yz + x’yz’ + xy’z’ + xy’z
Therefore, F(x, y, z) = x’y + xy’
yz x | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 7: Two- and Three-Variable Maps
Simplify the Boolean function: F(x, y, z) = (3, 4, 6, 7)
Therefore, F(x, y, z) = yz + xz’
yz x | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1

## Slide 8: Two- and Three-Variable Maps
Simplify the Boolean function: F(x, y, z) = (0, 2, 4, 5, 6)
Therefore, F(x, y, z) = z’ + xy’
yz x | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1

## Slide 9: Two- and Three-Variable Maps
Simplify the Boolean function:
F(A, B, C) = A’C + A’B + AB’C + BC
= A’C(B+B’) + A’B(C+C’) + AB’C + BC(A+A’)
= A’BC + A’B’C + A’BC’ + AB’C + ABC
= (1, 2, 3, 5, 7)
Therefore, F(A, B, C) = A’B + C
BC A | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0

## Slide 10: Four-Variable Map
The map minimization of four-variable Boolean functions is similar to the method used to minimize three-variable functions.
The map is considered to lie on a surface with the top and bottom edges, as well as the right and left edges, touching each other to form adjacent squares.
yz wx | 00 | 01 | 11 | 10
00 | m0 | m1 | m3 | m2
01 | m4 | m5 | m7 | m6
11 | m12 | m13 | m15 | m14
10 | m8 | m9 | m11 | m10

## Slide 11: Four-Variable Map
Simplify the Boolean function:
F(w, x, y, z) = (0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
Therefore, F(w, x, y, z) = y’ + w’z’ + xz’
yz wx | 00 | 01 | 11 | 10
00 | 1 | 1 |  | 1
01 | 1 | 1 |  | 1
11 | 1 | 1 |  | 1
10 | 1 | 1 |  | 

## Slide 12: Five-Variable Map
For five-variable maps, we need 32 squares.
The rows and columns are numbered in a reflected-code sequence.
 | 000 | 001 | 011 | 010
00 | m0 | m1 | m3 | m2
01 | m8 | m9 | m11 | m10
11 | m24 | m25 | m27 | m26
10 | m16 | m17 | m19 | m18
110 | 111 | 101 | 100
m6 | m7 | m5 | m4
m14 | m15 | m13 | m12
m30 | m31 | m29 | m28
m22 | m23 | m21 | m20
AB
CDE

## Slide 13: Five-Variable Map
Simplify the Boolean function F(A, B, C, D, E) = Ʃ(0, 2, 4, 6, 9, 11, 13, 15, 17, 21, 25, 29, 31)
F(A, B, C, D, E) = BE + AD’E + A’B’E’
 | 000 | 001 | 011 | 010
00 | 1 |  |  | 1
01 |  | 1 | 1 | 
11 |  | 1 | 1 | 
10 |  | 1 |  | 
110 | 111 | 101 | 100
1 |  |  | 1
 | 1 | 1 | 
 | 1 | 1 | 
 |  | 1 | 
AB
CDE

## Slide 14: Product of Sums Simplification
For this case we combine the squares which are marked as 0’s.
For example: F(A, B, C, D) = (3, 4, 6, 7, 11, 12, 13, 14, 15)
Therefore F(A, B, C, D) = (A’+B’)(C’+D’)(B’+D)
CD AB | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 1
01 | 0 | 1 | 0 | 0
11 | 0 | 0 | 0 | 0
10 | 1 | 1 | 0 | 1

## Slide 15: NAND and NOR Implementation
NAND and NOR gates are easier to fabricate with components.
Because of the prominence of NAND and NOR gates in the design of digital circuits, rules and procedures have been developed for the conversion from Boolean functions given in terms of AND, OR and NOT into equivalent NAND and NOR logic diagrams.

## Slide 16: NAND Implementation
Implement the function F = AB + CD + E using NAND gates.
The function F can be written as F = [(AB)’.(CD)’.E’]’

## Slide 17: NAND Implementation
Implement the following function with NAND gates.
F = (0, 6)
F’ = x’y + xy’ + z
F’ = ((x’y)’.(xy’)’.(z)’)’
F = (((x’y)’.(xy’)’.(z)’)’)’
yz x | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1

## Slide 18: NOR Implementation
Implement the following function with NOR gates.
F = (0, 6)
F’ = x’y + xy’ + z
F = (x + y’)(x’ + y)z’
F’ = (x + y’)’ + (x’ + y)’ + z
F = ((x + y’)’ + (x’ + y)’ + z)’
yz x | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1

## Slide 19: Don’t Care Conditions
In practice, there are some applications where the function is not specified for certain combinations of the variables.
Functions that have unspecified outputs for some input combinations are called incompletely specified functions.
In most applications, we simply don’t care what value is assumed by the function for the unspecified minterms.
These don’t care conditions can be used on a map to provide further simplification of the Boolean expression.

## Slide 20: Don’t Care Conditions
Simplify the function F = (1, 3, 7, 11, 15) has the don’t care conditions d = (0, 2, 5)
F = yz + w’x’ F = yz + w’z
yz wz | 00 | 01 | 11 | 10
00 | X | 1 | 1 | X
01 | 0 | X | 1 | 0
11 | 0 | 0 | 1 | 0
10 | 0 | 0 | 1 | 0
yz wz | 00 | 01 | 11 | 10
00 | X | 1 | 1 | X
01 | 0 | X | 1 | 0
11 | 0 | 0 | 1 | 0
10 | 0 | 0 | 1 | 0

## Slide 21: Determination of Prime Implicants
The process compares each minterm with every other minterm.
If two minterms differ in only one variable, that variable is removed and a term with one less literal is found.
This process is repeated for every minterm until the exhaustive search is completed.

## Slide 22: Determination of Prime Implicants
Simplify the function F = (0, 1, 2, 8, 10, 11, 14, 15) by using the tabulation method.
F = w’x’y’ + x’z’ + wy