## Slide 1: Digital Logic Design
Chapter 5
Combinational Logic with MSI and LSI

## Slide 2: Multiplexer
A digital multiplexer is a combinational circuit that selects binary information from one of many input lines and directs it to a single output line.
The selection of a particular input line is controlled by a set of selection lines.
For n selection lines, there are 2n input lines.

## Slide 3: Multiplexer
Multiplexer is abbreviated as MUX.
Logic diagram of a 4-to-1 line multiplexer:

## Slide 4: Multiplexer
Multiplexer can be constructed from a decoder.
2n input lines are added to n-to-2n decoder, one to each AND gate.
Finally the outputs of AND gates are applied to a single OR gate to make 1 output line.
The logic diagram is left for you as exercise.

## Slide 5: Multiplexer
Construct an 81 MUX using two 41 MUXs.

## Slide 6: Boolean Function Implementation
If we have a Boolean function of n+1 variables, we take n of these variables and connect them to the selection lines of a multiplexer.
The remaining single variable of the function is used for the inputs of the multiplexer.
For example: F(A, B, C) = Ʃ(1, 3, 5, 6)

## Slide 7: Boolean Function Implementation
For another example: F(A, B, C) = Ʃ(1, 2, 4, 5)

## Slide 8: Boolean Function Implementation
Implement the function F(A, B, C, D) = Ʃ(0, 1, 3, 4, 8, 9, 15)

## Slide 9: Read Only Memory (ROM)
A ROM is a device that includes both decoder and OR gates within a single package.
It consists of n input lines and m output lines.
Each bit combination of the input variables is called an address.
Each bit combination that comes out of the output lines is called a word.
For n variables, there are 2n distinct addresses and for each address, there is a word. It is named as 2nm ROM.

## Slide 10: Read Only Memory (ROM)
For a 256 ROM, the specification can be
  328 ROM or
  644 ROM or
  1616 ROM ….
The input variables n can be 5(25 = 32) or 6(26 = 64) or 4(24 = 16)…
The output lines m will be 8 or 4 or 16 …

## Slide 11: Read Only Memory (ROM)
ROM contains permanent binary information. It contains electronic fuses which are programmed by the designer.

## Slide 12: Combinational Logic Implementation
Implement the following functions with a ROM.
F1(A0, A1) = Ʃ(1, 2, 3) and F2(A0, A1) = Ʃ(0, 2)
Solution: As there are 2 inputs and 2 outputs, the size of ROM is 42. (For AND-OR gates)

## Slide 13: Combinational Logic Implementation
Implement the following functions with a ROM.
F1(A0, A1) = Ʃ(1, 2, 3) and F2(A0, A1) = Ʃ(0, 2)
Solution: As there are 2 inputs and 2 outputs, the size of ROM is 42. (For AND-OR-INVERT gates)

## Slide 14: Combinational Logic Implementation
Design a combinational circuit using a ROM. The circuit accepts 3-bit number and generates an output binary number equal to the square of the input number.
Solution: First we need the truth table. But we must not be naive in designing the circuit.

## Slide 15: Combinational Logic Implementation
As it accepts 3-bit number, input variable n will be 3. So 23 = 8.
The output lines can be 8, as we have 6 outputs. But that can be reduced to 4 technically.

## Slide 16: Programmable Logic Array (PLA)
A combinational circuit may have don’t care conditions which become address inputs that will never occur.
It is more economical to use a second type of LSI component called a programmable logic array (PLA).
It consists of n inputs, m outputs, k product terms and m sum terms.

## Slide 17: Programmable Logic Array (PLA)
PLA with three inputs, three product terms and two outputs implemented with combinational circuit is shown:

## Slide 18: Programmable Logic Array (PLA)

## Slide 19: Programmable Logic Array (PLA)
Implement the functions with a PLA having three inputs, four product terms and two outputs.
F1 = Ʃ(3, 5, 6, 7) and F2 = Ʃ(0, 2, 4, 7)