## Slide 1: Memory-mapped I/O and peripheral I/O
Memory Mapped I/O
1. 16-bit device address 2. Data transfer between any general-purpose register and I/O port. 3. The memory map (64K) is shared between I/O device and system memory. 4. More hardware is required to decode 16-bit address 5. Arithmetic or logic operation can be directly performed with I/O data
6. Control Signals used are like MEMR(bar), MEMW(bar)
7. Instructions used are like STA,STAX,LDA,LDAX
Peripheral Mapped I/O
1. 8-bit device address 2. Data is transfer only between accumulator and I.O port 3. The I/O map is independent of the memory map; 256 input device and 256. output device can be connected 4. Less hardware is required to decode 8-bit address 5. Arithmetic or logical operation cannot be directly performed with I/O data
6. Control signals used are like IOR(bar), IOW(bar)
7. Instructions used are like IN,OUT