## Slide 1: Robot Languages and Programming
Robot languages have been developed for ease of control of motions of robots having different structures and geometrical capabilities.
Some of the robot languages have been developed by modifying the existing general­ purpose computer languages and some of them are written in a completely new style.
Some of the programming languages are: WAVE, AL, VAL, AML, MCL, RAIL, HELP, RPL, PAL and ADA.
WAVE and AL
WAVE, developed at Stanford, demonstrated a robot hand-eye coordination while it was implemented in a machine vision system.
WAVE incorporated many important features. Trajectory calculations through coordination of joint movements, end-effector positions and touch sensing were some of the new features of WAVE. But the algorithm was too complex and not user-friendly. They could not be run in real-time and on-line. On the other hand, trajectory calculations are possible at compile time and they can be modified during run-time.
AL is a more powerful language and was developed to control robot arms.
It has a source language, a translator to generate runnable code and a run time system for effecting various motions of the robot manipulator. The syntax of the language can implement various subroutines, involving activities between the robot and its surroundings, various statements concerning SIGNALS and WAIT to carry on tasks in sequence. Different sensors can be incorporated and programming can take care of some condition monitoring statements. The robot manipulator movement-commands include various motions, velocities, forces, torques, etc. POINTY is another interactive system and a part of AL System.
Both are developed in Stanford Artificial Intelligence Laboratory .

## Slide 2: Robot Languages: VAL
VAL is a popular textual robot language developed by Unimation Inc. for the PUMA series of robots.
VAL has been upgraded to VAL II system with more interlocking facilities.
Victor Sheinman developed VAL language.
VAL is very user-friendly. It provides arm movement in joint, world and tool coordinates, gripping and speed control.
WAIT and SIGNAL commands can be given to implement a specific task. The commands are subroutines written in BASIC and translated with the aid of an interpreter. Compiled BASIC has more flexibility.

## Slide 3: Robot Languages: AML
A manufacturing language, AML was developed by IBM.
AML is very useful for assembly operations as different user-robot programming interfaces are possible. The programming language AML is also used in other automated manufacturing systems.
The advantage of using AML is that integers, real numbers and strings can be specified in the same aggregate which is said to be an ordered set of constants or variables. An aggregate can be used to specify coordinate values of the robot's joints or wrist position and orientation.

## Slide 4: Robot Languages: MCL
US Air force ICAM project led to the development of another manufacturing control language known as MCL by McDonnel-Douglas.
This is a modification of the popular APT (Automatically Programmed Tooling) language used in CNC machine tools as many similar commands are used to control machine tools in CAM applications.
Lines, circles, planes, cylinders and many other complex geometrical features can be defined in MCL.

## Slide 5: Robot Languages: RAIL
RAIL was developed by Automatix for robotic assembly, inspection, arc welding and machine vision.
A variety of data types as used in PASCAL can be used. An interpreter is used to convert the language into machine language commands.
It uses Motorola 68000 type microcomputer system. It supports many commands and control of the vision system.

## Slide 6: Robot Languages: HELP and JARS
HELP was developed by General Electric Company.
It acts more or less like RAIL.
It has the capability to control two robot arms at the same time. The structure of the language is like PASCAL.
JARS was developed by NASA's JPL.
The base of the language is PASCAL. JARS can be interfaced with PUMA 6000 robot for running robotic programs.

## Slide 7: Robot Languages: RPL
RPL was developed at SRI International.
A compiler is used to convert a program into the codes that can be interpreted by an interpreter.
Unimation PUMA 500 can be controlled with the. help of RPL.
The basic ideas of LISP (an AI language) have been organized into a FORTRAN-like syntax in RPL. It is modular and flexible.

## Slide 8: Robot Languages: Others
Besides these, there are some other languages like PAL, ADA etc.
PAL has been written by Richard Paul by modifying WAVE and incorporating features of PASCAL. But the representations of syntaxes used in the program are difficult to handle.
ADA developed by the Department of Defence (DOD) in USA is a real-time system that can be run on several microcomputers like Zilog, VAX, Motorola 68000, etc. ADA is convenient for controlling the robots used in a manufacturing cell.
.

## Slide 9: Robot Languages: Comparison
Different textual robot languages have different attributes.
For example, VAL, HELP and MCL though powerful for many simple tasks, do not have the same structured modular programming capability like AL, AML, JARS and ADA or VAL II.
In a manufacturing cell, multiple robots or robotic equipment work in unison. Control of two or more operations done by the robots in a coordinated manner is complex. Synchronizing the motions of the robots requires necessary software commands. AL, ADA, AML, MCL have the capability of controlling multiple arms.
The programming language must be capable of expressing various geometric features like joint angles, coordinate transformations such as rotation, translation, and vector quantities. Homogeneous matrices are used to specify the rotation. Rotation can also be specified by Euler angles. AML, RAIL and VAL Use Euler angles while AL manipulates homogeneous matrix for control.
AL is very suitable for assembly tasks wherein many sensors are employed, though other languages like AML and HELP are flexible enough to run various subroutines.
Stewing and straight ­line motions control are available with most of the languages.
However, in all the robot languages, features like editor, interpreter, compiler, data management, debugging are common

## Slide 10: CLASSIFICATION OF ROBOT LANGUAGES
Robot languages can be grouped broadly into three major classes:
1. First generation language
2. Second generation language
3. World modeling and task-oriented object level language
The first generation language provides an off-line programming in combination with the programming through robot pendant teaching.
VAL is an example of a first generation robot programming language.
The capability of a first generation language is limited to the handling of sensory data (except ON/OFF binary signals) and communication with other computers.
However, branching, input/output interfacing and commands leading to a sequence of movements of arm and body, and opening and closing of the end-effectors are possible.

## Slide 11: CLASSIFICATION OF ROBOT LANGUAGES
The second generation languages include AML, RAIL, MCL, VAL II etc.
They are structured programming languages performing complex tasks. Apart from straight line interpolation, complex motions can be generated with the second generation languages.
They can handle both analog and digital signals besides the binary signals. Force, torque, slip and other sensors can be incorporated on the joints, wrist or the gripper fingers and the robot controller is capable of communicating with such sensory devices so that better motion control can be effected.
In case of faults or errors, robots with second generation language programming can recover in the event of malfunction, probably by activating some other programs. This is of course, low level intelligence.
Robots programmed with second generation languages behave somewhat intelligently because of enhanced sensory capabilities.
Second generation languages have the added advantage of better interacting facilities with other computers. Data processing, file management and keeping all the records of events happening in the work-cell can be done more efficiently.

## Slide 12: CLASSIFICATION OF ROBOT LANGUAGES
A more advanced future language is `world' modelling. In this case, a task is defined through a command, say `TIGHTEN THE NUT'. The robot should be capable of performing step by step functions to accomplish the objective of tightening the nut.
This is possible only if the robot is capable of seeing the world around it. The three-dimensional model of the work environment around the robot must be understood.
The robot must find the nut and the spanner, pick them up and place them in a sequential manner and finally tighten the nut with the aid of the spanner.
Intelligence is required in this case and the robot should be capable of making decisions.
Future generation robot languages involve technology of artificial intelligence and hierarchical control systems.
It is hoped that it will be possible to develop complete off-line robot programming through world modeling and a high level object oriented command (say TIGHTEN THE NUT) will be obeyed by the robots.

## Slide 13: COMPUTER CONTROL AND ROBOT SOFTWARE
The program and control methods are actuated through software running on an operating system in which manipulation of data takes place. Monitors are used to activate control functions. In a robot, there are three basic modes of operation:
1. Monitor mode
2. Run mode or execute mode
3. Editor mode
The above modes constitute the operating system.

## Slide 14: Monitor Mode and Edit Mode
In the monitor mode, the programmer can define locations, load a particular piece of information in a particular register, store information in the memory, save, transfer programs from storage into computer control memory, enable or disable, and move back and forth into its edit and run mode.
In the edit mode, the programmer can edit or change a set of instructions of existing programs or introduce a new set of information. The user can erase some instructions and can replace them by new lines. In this mode, any error if shown on the monitor can be corrected. However, to come out of the edit mode, an end command, say (E) should be given.

## Slide 15: Run or Execute Mode
The programs to carry out a predefined task can be executed in the run mode. The sequential steps as written by the programmer are followed during the run mode.
Sometimes dry run can be tested by making the switch disable. For example, when arc welding is done, the trajectory can be tested by dry run after the weld signals are made non-operational. The signals are made non-operational by the disable switch. After dry run, the switch may be made operational by the instruction enable.,
A program can be tested in run mode and by debugging, the errors in the program can be rectified.
Suppose the robot has been programmed to describe a path beyond the defined envelope, the robot cannot move and the monitor will exhibit some error message.
The path or the coordinate points of locations are to be redefined and corrected in the edit mode. Then after ending the edit mode, the run mode may be actuated.
The robot will run following the correct trajectory.